RISK ASSESSMENTS

INDEX

# 1.		ASBESTOS REMOVAL

2.		BRICKS, Palletised, Storage and Stacking

3.		BRICKS, Palletised, Storage on Scaffolds

4.		BLOCK LAYING, High Density

5.		CARRYING PLUMBING TANKS, BOILERS, RADIATORS, LEAD ROLL etc.

6.		CEMENT MIXING  Silo operated Ready Mix

7.		CONCRETE – Scabbling

8.		CRANES, Lifting Loads

9.		CROSSCUT SAW

10	.	Rip Saw, Planing Machine

11.		CUTTING with STIHL SAW

12	.	DEMOLITION

13.		DEMOLITION SURVEYS

14.		DIAMOND CUTTING

15.		DUMPER OPERATIONS

16.		ELECTRIC ARC WELDING

17.		ELEVATED WORK PLATFORM

18.		EXCAVATIONS

19.		FORKLIFT SIDE LOADERS

20	.	FORKLIFT COUNTER BALANCE/TELESCOPIC/ROUGH TERRAIN

21.		GLAZING, Installation

22.		GLAZING, Stripping  out

23.		GRINDING with Twin Shaft Grinder

24.		HOISTS, Working with

25	.	KANGO CHISEL

26	.	LADDERS – Work from

27	.	LAYING SLABS AND KERBS

28.		LEAD WORK, Roll and Sheet

29	.	MAN MADE INSULATION, working with

30.		OXY-ACETYLENE CUTTING/WELDING

31	.	PAINTING, low level

32	.	PAINTING, SPRAY

33.		REFURBISHING BUILDINGS, Demolition

34.		ROAD REPAIRS

35.		ROOFS

36	.	SAW – Bench

37	.	SCAFFOLDS, Work on

38.		SCAFFOLDS, Work from Tower

# 39	.	SEWER, Entry into

40	.	SHUTTERS – Foundation

41	.	SHUTTERS – Vertical or System

42.		SITE TRANSPORT, Muck shifting

## RISK ASSESSMENT

ACTIVITY: Asbestos Removal

| SITE: | DATE: |
| --- | --- |

MAIN HAZARDS:

##### Inhalation of dust or fibres

Skin irritation

Eye irritation

Manual handling

CONTROL MEASURES

Work strictly to method statement

Only trained operatives be engaged

Use personal protection provided

Use site-changing facility

Report defects found in P.P.E

# INFORMATION TO EMPLOYEES

Refer to Construction Manual

Refer to H.S.E Guidance Notes

Construction health, Safety & Welfare Regulations 1996

#### PERSONAL PROTECTION

# Coverall with hood

Dust respirator, Safety Footwear

Eye Protection, gloves

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Palletised Bricks, Stacking on Scaffolds

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Falling loose bricks

Stacks collapsing or sinking

Obstruction to vehicles

Untrained forklift drivers

Danger to children

#### CONTROL MEASURES

Plan stacking area

Fit brick guards to scaffold

Do not overload scaffold

Stack neatly

Only trained forklift drivers to drive

Construction Health , Safety & Welfare Regulations 1996

#### INFORMATION TO EMPLOYEES

Verbal instruction

#### PERSONAL PROTECTION

Safety helmet, safety footwear, gloves

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Palletised Bricks – Storage and Stacking

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Falling loose bricks

Stacks collapsing or sinking

Obstruction to vehicles

Untrained forklift drivers

Danger to children

#### CONTROL MEASURES

Plan stacking area

Avoid soft uneven ground

Keep stacks to 2 high only

Only trained forklift drivers to drive

Construction, Health, Safety & Welfare Regulations 1996

#### INFORMATION TO EMPLOYEES

Verbal instruction

#### PERSONAL PROTECTION

Safety helmet, safety footwear, gloves

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Block Laying – High Density

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Manual handling

Back injuries

Trapping fingers

Strain on arms, wrists

Falls from heights

Falling materials

#### CONTROL MEASURES

Use good lifting procedures

Ensure hop-ups are adjusted to suit

Ensure scaffolds are complete and toeboards are in position

Use additional personnel to lift over 25 kg

#### INFORMATION TO EMPLOYEES

Refer to C.I.T.B. Manual

#### PERSONAL PROTECTION

Helmets, gloves, safety footwear

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Carrying Plumbing Tanks, Boilers, Radiators, Lead Rolls etc

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Falling down stairs

Slipping or tripping

Dropping load on feet

Manual handling of heavy loads

#### CONTROL MEASURES

Site storage container at ground level

Keep clear walking space in container

Seek help for heavy or awkward loads

#### INFORMATION TO EMPLOYEES

Verbal instruction

#### PERSONAL PROTECTION

Helmet, overalls, safety footwear

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Cement Mixing, Silo Operation Ready Mix

| SITE: | DATE: |
| --- | --- |

MAIN HAZARDS:

Trained operatives to operate mixing plant

Manual handling

Skin contact with dry and wet cement

Dust and noise

CONTROL MEASURES

Keep hands away from moving parts

Use barrier cream

Wash frequently

Close safety gates

Refer to C.O.S.H.H. assessment

# INFORMATION TO EMPLOYEES

# Verbal instruction and Training

Use of lockout procedure to carry out maintenance

Isolate power supply

#### PERSONAL PROTECTION

# Helmet, eye protection, gloves

Safety footwear, dust mask

Ear defenders may also be required

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Concrete – Scabbling

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Noise, dust, working from scaffolds

Manual handling

Flying particles

Dropping equipment

#### CONTROL MEASURES

Only trained operatives to be used

Check scaffolds are properly constructed

Ensure personal protective equipment is worn

Use anti-vibrating equipment and carry out assessment

#### INFORMATION TO EMPLOYEES

Verbal instruction

Noise assessment

Induction training

General site safety training

#### PERSONAL PROTECTION

Helmet, goggles, ear defenders, dust mask, safety footwear

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Lifting Loads with Cranes

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Overhead electrical services

Underground services

Slinging of loads

#### SAFETY INFORMATION

# Refer to C.I.T.B Manual,

HSE Guidance Note GS 6

Construction Health, Safety and Welfare Regulations 1996

#### CRANE AND DRIVER

Documentation must be inspected prior to lifting ie Certificate of past inspection within 14 months, Certificate of Lifting Appliance within 6 months and Drivers Certificate of Competence. Also, check SWL of chains, slings, etc

BANKSMAN

A trained conversant with lifting and slinging activities must be appointed to be in charge of the lifts.  The Banksman must be able to signal to the crane drivers by hand signals or radio link

#### PUBLIC SAFETY

Fence off an area to prevent members of the public coming into the hazard area and display warning notices

#### TRAFFIC

Take into consideration, areas where traffic could be at risk with an overhead load.  If necessary, set up a traffic management system

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Crosscut Saw

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Contact with blade

Noise, dust

Flying particles

#### CONTROL MEASURES

Only trained operatives to use

Check guards are in position

Ensure extraction is working

Ensure emergency stop is functioning

Ensure lighting is up to standard

Wear personal protection

#### INFORMATION TO EMPLOYEES

Remember training rules

Refer to Woodworking Regulations

Report defects to workshop manager or supervisor

#### PERSONAL PROTECTION

Eye protection, ear protection, overalls, safety footwear

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Rip Saw, Planing Machines

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Contact with saw blade

Tripping

# Noise and dust

Vibration

#### CONTROL MEASURES

Keep work areas clear of materials

Only trained operatives to use

Ensure ventilation hood is operating

Carry out vibration assessment

Use anti-vibration equipment

Wear personal protection

#### INFORMATION TO EMPLOYEES

Refer to Woodworking Machinery Regulations

C.I.T.B. manual

H.S.E. information sheets 1-10

#### PERSONAL PROTECTION

Eye protection, ear protection, overalls safety footwear, dust mask

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Cutting with Stihl Saw

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Disc disintegrating

Flying particles

Dust, noise, fumes

Contact with revolving disc

#### CONTROL MEASURES

Trained operatives to mount disc

Use correct start up procedure

Use correct grade and type of disc

Use protective equipment

Use vibration suppressed equipment

#### INFORMATION TO EMPLOYEES

Implement training instructions

Report defects

Carry out vibration assessment

#### PERSONAL PROTECTION

Safety helmet, eye protection, ear protection, dust mask, safety footwear

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Demolition

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Overhead electrical services

Underground gas services

Flammable materials – dust, fumes etc

Toxic wastes

Asbestos, lead, lead paint

Vessels, tanks, flues

Falls from heights

Struck by falling materials

Noise, collapse of structures

#### SAFETY INFORMATION

# Refer to H.S.E GS29 Sections 1-4

BS6187

Detailed method statements

Health, Safety & Welfare Regulations 1996

#### CONTROL MEASURES

# Only trained and experienced operatives to be employed

Fence off area and display warning notices

Install temporary shoring as required

Provide suitable edge protection as required

Work to the method statement

#### MEMBERS OF THE PUBLIC

All necessary steps will be taken to prevent dust or other materials from being a hazard to the public e.g. use water spray, sheet over transport leaving the site

RESTRICTED AREAS AND SAFE DISTANCES

# To be determined prior to commencement of work

#### SEQUENCE OF EVENTS

# To be planned ahead and contained in the method statement

INFORMATION TO EMPLOYEES

# Verbal instruction from supervisor

A copy of method statement plus copies of GS29 and Construction Safety Manual to be kept for reference ON SITE

#### PERSONAL PROTECTION

Safety helmet, safety footwear, eye protection, ear protection, overalls, dust mask, safety harness

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Demolition Surveys

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Weakened floor

Holes in floor

Dark areas

Dust or chemicals

Flammable residues

Toxic residues

SAFETY INFORMATION

# Refer to Construction Safety Manual:

CONTROL MEASURES

Check history of building

Do not survey alone

Take a good flash lamp

Avoid obvious weakened floors, stairways etc

#### INFORMATION TO EMPLOYEES

Display warning notices

Prepare a detailed method statement

#### PERSONAL PROTECTION

Safety helmet, safety footwear, overalls

Other protection may be required e.g. dust masks, ear protection, and eye protection

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Diamond Cutting

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Contact with revolving components

Manual handling

Noise, dust

Falls from heights

Vibration

#### CONTROL MEASURES

Work from a safe platform e.g. scaffold

Ensure ladders are secured

Seek assistance with heavy objects

Check guards are in position

Vibration suppressed equipment

#### INFORMATION TO EMPLOYEES

Only trained personnel to operate

Follow supervisor’s instructions

Report defects

Vibration assessment

Noise assessment

#### PERSONAL PROTECTION

Helmet, goggles, ear protection, safety footwear

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Dumper Operations

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Dumper falling into trench

Speeding and careless driving

Overloading the skip

Noise and fumes

#### CONTROL MEASURES

Only trained drivers up to C.I.T.B standard to operate machines

Regular maintenance and servicing

Drivers route to be planned and marked

Fit stop blocks at trenches

#### INFORMATION TO EMPLOYEES

Refer to C.I.T.B. Plant Operators Handbook

Follow Supervisor’s instructions

Report all defects

#### PERSONAL PROTECTION

Safety helmet, ear defenders, eye protection, safety footwear

In dusty conditions, a dust mask may be required

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Electric Arc Welding

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Inhalation of fumes

Weld flash

Radiation burns

Hot sparks, fire, burns from hot metal

Electric shock

#### CONTROL MEASURES

Only trained operatives to use

Ensure local exhaust ventilation is working

Wear recommended personal protection

Keep area clear of combustible materials

Use flash screens

#### INFORMATION TO EMPLOYEES

Verbal instruction and training

Refer to Safety Policy

#### PERSONAL PROTECTION

Welding helmet, leather type apron, gauntlet type gloves, overalls, safety footwear

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Operation of Elevated Work Platform

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Fall from platform

Fall of materials

Crushing from overhead obstructions

Uneven ground and drain covers

Injuries to other contractors, public

#### CONTROL MEASURES

Only trained and experienced personnel to operate the machine

Harness should be secured

Keep work platform clean

Ensure hand tools are prevented from falling

Fence off work area and post warning notices

#### INFORMATION TO EMPLOYEES

Carry out maintenance check

Carry out safety checks ie brakes, steering, and tyres

Do not operate defective equipment

Look out for obstruction

#### PERSONAL PROTECTION

Safety helmet, safety footwear, safety harness, eye protection

Ear protection may be required

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Excavations

| SITE: | DATE: |
| --- | --- |

#### SAFETY INFORMATION

# Refer to C.I.T.B. Manual

#### DETERMINE:  TRENCH DESIGN FEATURES

# Unsupported

Battered back

Benched Down

Support System

#### ELECTRICAL SERVICES

Work in proximity of overhead electrical power lines

# Refer to C.I.T.B. Manual, Section 20, 24, 25

# H.S.E. Guidance note GS 6

#### WORK IN PROXIMITY OF UNDERGROUND SERVICES

# Refer to C.I.T.B manual

H.S.E. Guidance note GS6

INFORMATION TO OPERATIVES

Must be given clearly and questions should be asked by the supervisor to ensure instructions have been understood.

#### ACCESS TO EXCAVATIONS

# Suitable ladders must be provided or a “Walk in area” at the end of the trench

#### PERSONAL PROTECTION REQUIRED

Will be determined by the site supervisor but must include:

a)	 safety helmet

b)	safety footwear

c)	gloves

Dust masks, foul weather clothing and ear protection may also be required

#### PUBLIC SAFETY

Excavations and open manholes require to be fenced off at the end of the working day, or made safe by other means e.g. backfilling trenches and fitting temporary manhole covers.

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Forklift side Loader

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Striking against operative

Overturning forklift

Hazardous stacking

Noise

#### CONTROL MEASURES

# Only trained and certificated operatives to drive

# Ensure adequate lighting

Regular maintenance of machines

#### INFORMATION TO EMPLOYEES

As per R.T.I.T.B training

#### PERSONAL PROTECTION

Helmet, eye protection, safety footwear

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Forklift Counter Balance and Telescopic Rough Terrain

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Striking against operatives

Overturning forklift

Hazardous stacking

Noise

Soft Ground

#### CONTROL MEASURES

Only trained and certificated operatives to drive to C.I.T.B standard

Ensure adequate lighting

Regular maintenance of machines

#### INFORMATION TO EMPLOYEES

# As per C.I.T.B. training

#### PERSONAL PROTECTION

Helmet, eye protection, safety footwear, gloves and overalls

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Installation of Glazing at Low Level

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Tripping when carrying panels

Falls from trestle scaffold

Dropping a panel

#### CONTROL MEASURES

# Keep work area clear of rubbish

Lift panels evenly, no sudden movements

Ensure trestle scaffolds are even

Use only 110v tools

#### INFORMATION TO EMPLOYEES

Supervisor’s verbal  instructions

Refer to method statement

#### PERSONAL PROTECTION

Helmet, eye protection, safety footwear, gloves

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Stripping Out Existing Glazing (Low Levels)

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Breaking glass

Falling glass

Falling frames

Falls from trestles

Electrical hand tools

Dust from drilling

Nails in timber

#### CONTROL MEASURES

# Barricade work area

Experienced operatives only to be engaged in this activity

De-nail timbers

Keep work area clear of broken glass

#### INFORMATION TO EMPLOYEES

Supervisor’s verbal instruction

Refer to method statement

#### PERSONAL PROTECTION

Helmet, safety footwear, gloves, eye protection

Dust masks may be required for drilling

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Grinding with Twin Shaft Grinder

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Contact with revolving stone

Flying particles

Inhalation of dust

Exposure to noise

#### CONTROL MEASURES

Only trained operatives to use

Ensure guards are in place and secure

Dress stones regularly

Set tool rest as near as possible to the stone

Ventilation to capture dust at source

#### INFORMATION TO EMPLOYEES

Verbal instruction and training

Refer to Safety Policy

Refer to Factories Act

#### PERSONAL PROTECTION

#### Eye protection to BS. 2092

Safety footwear

Dust mask and ear defenders may also be required

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Breaking out concrete with Kango Chisel or similar tool

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Noise, dust

Flying particles

Falls from heights

Falls of concrete cuttings

Dropping the tool

Electric shock

Vibration

#### CONTROL MEASURES

# Use only 110v equipment

Check equipment is in good condition

Work only from safe access platforms

#### INFORMATION TO EMPLOYEES

Verbal instruction

Tool box safety reminder

Report all defects

Vibration assessment

#### PERSONAL PROTECTION

Safety helmet, safety footwear, eye protection, ear protection, dust mask

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Work from Ladders

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Falls from heights

Falling materials

Carrying materials

Ladder slipping

#### CONTROL MEASURES

# Use only ladders without defects

Ladder should extend 3’6” above the work platform

Safe angle of use 1:4

Secure at top or bottom

Foot ladder

#### INFORMATION TO EMPLOYEES

Verbal

#### PERSONAL PROTECTION

# Helmet, safety footwear and gloves are required

Goggles, dust masks and ear defenders may also be required.  Supervision will advise.

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Laying slabs and kerbs

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Manual handling

Trapping fingers

Trapping toes

Dust from cutting disc

Noise

#### CONTROL MEASURES

# Lift correctly

Seek help for very heavy slabs or kerbs

Use personal protection provided

Keep materials close to the job

#### INFORMATION TO EMPLOYEES

Refer to C.I.T.B. Manual

#### PERSONAL PROTECTION

Safety helmet, dust mask, safety footwear, ear defenders.

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Lead Work – Roll and Sheet

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Ingestion of lead particles

Manual handling of rolls and sheets

Working on roofs and sloping surfaces

Working form ladders

Working from scaffolds

Dust and fumes

#### CONTROL MEASURES

#### Wash hands before eating or smoking

Seek assistance for heavy rolls or sheets

Ensure roof ladders and edge protection is in place

# Ensure scaffolds are complete and secure

#### INFORMATION TO EMPLOYEES

Health, Safety and Welfare Regulations 1996

Verbal instruction site

Refer to C.O.S.H.H

Refer to C.I.T.B. Manual

Refer to Lead Work Regulations

#### PERSONAL PROTECTION

Helmet, overalls safety footwear.

Fume mask and eye protection may also be required if heating or burning lead

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Man Made Insulation – Working with

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Contact with fibre (irritant)

Inhalation of fibre (Long irritant)

#### CONTROL MEASURES

# Prevent skin contact

Wear personal protection

#### INFORMATION TO EMPLOYEES

Verbal instructions

Refer to C.O.S.H.H Assessment

Implement manufacturers Instructions

#### PERSONAL PROTECTION

Safety helmet, eye protection gloves, dust mask overalls

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Oxy-Acetylene Cutting/Welding

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Explosion

Fire

# Burns

Inhalation of fumes

#### CONTROL MEASURES

# Only trained operatives to use

Ensure valves and gauges are properly fitted

Ensure there are no leaks from valves , tubes or torches

Ensure flashback arrestors are fitted

Use recommended protective clothing

Ensure adequate ventilation at work area

#### INFORMATION TO EMPLOYEES

Report any defects

Refer to safety policy

Use screen in confined areas

Verbal instruction

#### PERSONAL PROTECTION

Welding goggles or full mask

Safety footwear

Gauntlet type gloves

Leather type apron may be required

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Painting

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Falls from ladders and trestles

Inhalation of vapour

Skin contact with paint and thinners

#### CONTROL MEASURES

# Ensure ladders are in good condition and properly secured

Ventilate areas by opening windows etc

Use barrier creams

Avoid confined spaces

#### INFORMATION TO EMPLOYEES

Refer to C.O.S.H.H. assessment

Refer to C.I.T.B Manual

#### PERSONAL PROTECTION

Overalls, eye protection, safety footwear

Fume mask may also be required

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Painting - Spray

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

Explosive mixtures

Fire, toxic fumes

Skin irritation

Inhalation of fumes

Manual handling

#### CONTROL MEASURES

# Exhaust ventilation

# FLP Lighting

Fire proof store

Personal protection

No smoking or naked lights

#### INFORMATION TO EMPLOYEES

Only trained personnel to operate

Manufacturers mixing instructions

Refer to warning notices

Refer to C.O.S.H.H. Assessment

Refer to Notice board

#### PERSONAL PROTECTION

Ventilated masks

Gloves

Safety footwear

Overalls

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Demolition Activities in Refurbishing Buildings

| SITE: | DATE: |
| --- | --- |

SAFETY INFORMATION

# H.S.E Guidance Notes GS 29 Parts 1/2/3/4

SERVICES

# Ensure electrical, gas water services are properly installed

#### PREVENTION OF COLLAPSE OF STRUCTURE

Prior to cutting or disturbing load bearing components

CHEMICAL /OIL SPILLAGE

Ensure if storage tanks are present that contents are identified before removal

Seek advice from safety consultant as soon as possible

#### HOLES IN FLOORS

Warning notices require to be displayed and temporary fencing may be required

C.O.S.H.H

Dust from demolition should be treated as toxic and toxic grade masks be provided

PERSONAL HYGIENE

Wash hands prior to eating.  DO NOT WEAR dust-laden clothing in eating areas

PUBLIC SAFETY

Erect fencing 2m high and display warning notices in areas where the public could be at risk.

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Road repairs, Environmental improvements

| SITE: | DATE: |
| --- | --- |

#### SAFETY INFORMATION

# Refer to chapter 8, Road Traffic Signs etc

Refer to C.I.T.B. manual

H.S.E.Guidance Note GS6

#### MAIN HAZARDS

Road transport and vehicles

Protection of members of the public

Noise

Underground services

#### PREVENTATIVE MEASURES

# Set up traffic management system

Fence off work areas and excavations

Carry out noise assessment

Use cable detection equipment

#### PERSONAL PROTECTION

# Safety helmet, hi visibility clothing, ear defenders, safety footwear, goggles

Dust masks, foul weather clothing may also be required

#### PUBLIC SAFETY

Excavations and open manholes require to be fenced off at the end of the working day, or made safe by other means ie backfilling trenches and fitting temporary manhole covers

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Work on roofs

| SITE: | DATE: |
| --- | --- |

#### SAFETY INFORMATION

# Health, Safety & regulations 1996

Refer to C.I.T.B. MANUAL,

H.S.E. Guidance Notes GS15, GS31, GS42 and HS (6) 33

#### MAIN HAZARDS

# Falls from heights

Materials falling

Storage and stacking of materials

#### PREVENTATIVE MEASURES

# A prepared method statement is required

Scaffolds and edge protection to be adequate for the risk

Ladders to be of adequate length, set to a proper angle 1:4 and properly secured

Suitable toeboards and brickguards to be fitted

Only suitably trained operatives to be engaged in this work

#### PERSONAL PROTECTION REQUIRED

# Safety helmet, safety footwear are essential

Safety harness and foul weather clothing may also be required

#### PUBLIC SAFETY

Fenced off areas and warning notices are required for areas where members of the public require to be isolated from the work area.

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Bench Saw

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Contact with blade

Noise, dust

Flying particles

#### CONTROL MEASURES

# Only trained operatives to use

Check guards are in position

Ensure extraction is working

Ensure emergency stop is functioning

Ensure lighting is up to standard

Wear personal protection

Ensure rear table 1.2m is in position

#### INFORMATION TO EMPLOYEES

Remember training rules

Refer to woodworking regulations

Report defects to workshop manager or supervisor

#### PERSONAL PROTECTION

Eye protection, ear protection

Overalls, safety footwear

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Work on scaffolds

| SITE: | DATE: |
| --- | --- |

#### SAFETY INFORMATION

# Construction Health and Safety Welfare Regulations 1996

# Refer to C.I.T.B. MANUAL

H.S.E. Guidance notes

#### MAIN HAZARDS

# Removal of components

Falls from heights

Overloading platforms

Falling materials

Falls from ladders

Scaffold collapse

#### CONTROL MEASURES

# Use only certificated erectors

Choose scaffold type to suit i.e. tube & fittings or system scaffold

Ensure scaffold is complete and handover certificate obtained

Inspect scaffold regularly

Replace any missing components

Complete 7-day inspection register

#### PERSONAL PROTECTION REQUIRED

Will be determined by Site Supervisor but must include:

a)	Safety helmet

b)	Safety footwear

c)	Gloves

OTHER PROTECTION

May be required e.g. foul weather clothing, dust mask, goggles, ear defenders

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Work from tower scaffolds

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Falls from heights

Falling materials

Overturned scaffold

Electric shock

#### CONTROL MEASURES

# Ensure assembly is complete before mounting scaffold

# Ensure overhead electrical supplies are isolated

#### INFORMATION TO EMPLOYEES

Refer to manufacturer’s specification

Dismount scaffold before moving

Do not overload scaffold

Watch out for windy conditions

#### PERSONAL PROTECTION

Helmet, safety footwear are required

Goggles, dust masks and ear defenders may also be required

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Entry into sewer/confined spaces

| SITE: | DATE: |
| --- | --- |

#### SAFETY INFORMATION

Refer to C.I.T.B. Manual

#### VENTILATION

# Where possible open manhole on either side of the one to be entered

#### Atmospheric Test

# Ensure this is carried out prior to entering the manhole

#### Remember

Methane CH(		is lighter than air

Hydrogen Sulphide H2S		is heavier than air

Carbon Monoxide CO		is heavier than air

Carbon Dioxide CO2		is heavier than air

#### NOTE

If gas is detected NO ONE must enter the sewer or manhole.  Seek help from Head Office.

#### RESCUE EQUIPMENT

Operatives entering the manhole or sewer must wear full “Parachute” harness and a rescue line attached.  The gas monitor must also be taken with them.  A standby man must be on watch to raise the alarm and seek help in the event of an emergency.

#### PERSONAL HYGIENE

Wash hands thoroughly prior to eating.  DO NOT take soiled clothes into the eating area.

#### FIRST AID

Ensure all cuts and abrasions are cleaned and covered with an adhesive dressing.  Report all cuts and abrasions.

#### WEIL’S DISEASE

Should anyone become unwell with a “flu-like” illness, inform your Doctor that you have been working in a sewer.

#### PERSONAL PROTECTION

Strict adherence to wearing protective equipment is required.

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Foundation shutters

| SITE: | DATE: |
| --- | --- |

MAIN HAZARDS

# Manual handling

Falls of material

Falls of persons (low level)

Excavation collapse

General site conditions

Wet concrete

#### CONTROL MEASURES

# Seek assistance for heavy or awkward lifts

Maintain clear access to work place

Separate work area if necessary

Provide banksman for mechanical lifts

Only experienced and trained operatives to be used

Work to manufacturers’ instructions

Report damaged components to supervisor

#### INFORMATION TO EMPLOYEES

# Verbal instructions

Refer to  CITB Manual

Manufacturer’s instruction

#### PERSONAL PROTECTION

Helmet, goggles, dust mask, safety footwear and gloves are required

Ear defenders may also be required,

Supervision will advise.

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]  Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

| ACTIVITY: Vertical or System Shutters |
| --- |
| SITE: | DATE: |

#### MAIN HAZARDS

# Falls from heights

Manual handling

Falls of material and components

General site conditions

Weather conditions

Wet concrete, shutter oils

#### CONTROL MEASURES

# Work to design features

Work to manufacturers’ instructions

Provide banksman to control lifts

Separate work area if practical

Experience and trained operatives to be employed on this type of work

Provide suitable access ladders

Provide suitable work platforms or scaffolds

#### INFORMATION TO EMPLOYEES

# Verbal instructions

Refer to CITB Manual

Refer to method statement

Manufacturer’s instruction

#### PERSONAL PROTECTION

# Helmet, safety footwear, gloves are required

Goggles, dust mask

Ear defenders may also be required

Supervision will advise

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title

## RISK ASSESSMENT

ACTIVITY: Site Transport (Muck shifting)

| SITE: | DATE: |
| --- | --- |

#### MAIN HAZARDS

# Vehicle collisions

Falling materials

Collision with personnel

Overturning vehicles

Reversing vehicles

#### CONTROL MEASURES

# Mark out safe route – tapes, notices

Advise all drivers

Define safe speed

Do not overload vehicles

Ensure reversing audible alarm is working

#### INFORMATION TO EMPLOYEES

# Verbal

Only certificated drivers to operate machines

#### PERSONAL PROTECTION

# Helmets, safety footwear, goggles ear defenders, foul weather clothing

If control measures are implemented, the risk of injury or illness is considered to be:  Low [  ]   Medium [  ]   High [  ]   (Tick)

Signed	     Job Title